Transport Layer
transport

---
Contents
- General concepts
  - Process to process delivery
  - Sockets
  - Multiplexing and demultiplexing
  - Pushing & Pulling
  - Flow Control
  - Error Control
  - Connectionless vs connection-oriented service
  - Reliable vs unreliable
- UDP vs TCP

---
Process to process delivery
- Transport layer:
  - Responsible for process-to-process delivery
  - Processes communicate using the client-server paradigm

---
Port Numbers
- Every server process listens at a certain port
- The client uses an ephemeral port for the reception of the replies

---
IP addrs. vs port nums
- The IP address indentifies the host
- The port identifies a particular process in the host

---
Sockets
- Combination of the IP + port
  - Uniquely define the process
  - Sockets → basic abstraction for network programming in most OS
# Connect to server
s.connect((HOST, PORT))

---
ICANN Ranges
- Well-known ports: 0 - 1023
  - Assigned and controlled by IANA
- Registered ports: 1024 to 49,151
  - Not assigned nor controlled by IANA
  - Registered with IANA to prevent duplication.
- Dynamic ports. 49,152 - 65,535
  - temporary or private port numbers.
https://www.iana.org/assignments/service-names-port-numbers/service-names-port-numbers.txt

---
Well-known ports
- In Unix stored in a file called /etc/services
- Example: ftp server
  - 2 port numbers
  - One for each different transport protocol

---
Well-known ports
DIY
$ less /etc/services
tcpmux 1/tcp # TCP port service multiplexer
echo 7/tcp
echo 7/udp
discard 9/tcp sink null
discard 9/udp sink null
systat 11/tcp users
daytime 13/tcp
daytime 13/udp
netstat 15/tcp
qotd 17/tcp quote
msp 18/tcp # message send protocol
msp 18/udp
….
$ grep domain /etc/services
domain	53/tcp	# Domain Name Server
domain	53/udp
Explore the file
/etc/services

---
Well-known ports
DIY
$ less /etc/services
tcpmux 1/tcp # TCP port service multiplexer
echo 7/tcp
echo 7/udp
discard 9/tcp sink null
discard 9/udp sink null
systat 11/tcp users
daytime 13/tcp
daytime 13/udp
netstat 15/tcp
qotd 17/tcp quote
msp 18/tcp # message send protocol
msp 18/udp
….
$ grep domain /etc/services
domain	53/tcp	# Domain Name Server
domain	53/udp
Explore the file
/etc/services

---
Encapsulation and decapsulation
Client
Server
Message
Message
Logical channel
H
Message
H
Message
Decapsulation
Encapsulation

---
Multiplexing and demultiplexing

---
Flow control: Pushing & pulling
- Delivery can occur in two ways
  - Push: producer delivers items when produced
    - No request from consumer
    - The consumer may be overwhelmed
      - Need for flow control
  - Pull: producer delivers items when requested
      - No flow control required

---
Flow control at the transport layer
- Sender: producer
- Transport layer at sender: producer & consumer
- Transport layer at sender: consumer & producer
- Receiver: consumer

---
Error control
- The network layer is unreliable
- When reliability is required at the transport layer, error control is responsible for:
  - Detect and discard corrupt packets
  - Keep track of lost and discarded packets (resend)
  - Discard duplicates
  - Buffer out-of-order packets
- Implemented through:
  - Sequence numbers (in packets)
  - Acknowledgement and timers

---
Connectionless protocols
- Message divided into chunks (datagrams) by the application layer
- Each datagram treated as a single unit
  - Independent from the rest
  - Encapsulated as a packet by the transport layer
- Packets sent in order
- Reception may be out of order
  - Problem because no sequence numbers
  - Neither error control

---
Connectionless protocols

---
Connection-oriented protocols
- First establishment of logical connection
  - End to end service
- May be implemented even over connectionless protocols at the network layer
- Can implement flow & error control

---
Connection-oriented protocols

---
Transport layer protocols in TCP/IP suite

---
User Datagram Protocol (UDP)
- Connectionless
- Unreliable
- Very simple => minimum overhead
- Control can be provided by the Aplication Layer

---
Well-known ports used with UDP

---
User Datagram
- Fixed size header of 8 bytes
- Mainly used for the specification of ports
- Optional checksum
- Up to 64KB size

---
UDP
- Connectionless protocol
  - Messages not numbered
- No flow control
- No error control
  - Except for the checksum. Wrong packets discarded
- No congestion control
- Flow control or error control might by provided at the application layer

---
UDP Queues

---
Transmission Control Protocol (TCP)
- Connection-oriented
- Reliable
  - based on GBN approach
  - Use of checksums
  - Retransmission of lost or corrupted packets
  - Cumulative and selective ACKs
- Complex protocol with multiple phases
  - Connection establishment
  - Data transfer
  - Connection teardown
- Full-duplex communication
  - Data flows in both directions at the same time

---
Well-known ports used with TCP

---
Stream delivery service
- Stream oriented protocol
  - Two processes connected by imaginary tube
- Sending & receiving circular buffers
- Data is sent in packets called segments
Stream of bytes

---
Numbering system
- All bytes are numbered
  - Numbering independent in each direction
  - Arbitrary start number
- Sequences are also numbered
  - Number of the first data byte contained
  - Some special cases for control messages

---
Numbering system
- Segments also include an acknowledgement number:
  - Number of the next byte expected
- Cummulative numbering:
  - Example: ack number = 5643
    - All bytes from the beginning up to 5642 received
    - Doesn’t mean a total number of 5642 received
    - The initial one is random and therefore probably not 0

---
TCP Segment

---
TCP Segment
- Sequence Number
  - Starting at a random Initial Sequence Number (ISN)
- Header Length:
  - Number of 4-byte words in the header
  - Total number of bytes = HLEN * 4
- Control
  - Flags for connection establishment & control flow

---
TCP Segment
- Window size:
  - Max 65535 bytes
  - Set by the receiver (rwnd)
  - The sender must obey dictation of the receiver
- Checksum:
  - Mandatory in TCP
- Urgent pointer: valid when urgent flag set
  - Value to be added to sequence number to get the last urgent byte
- Options: up to 40 extra bytes

---
TCP Connection
- Logical path establishment between source and destination
- Three phases:
  - Connection establishment
  - Data transfer
  - Connection termination

---
Connection Establisment
Three way handshaking
No data but consume 1 seq number
ISN
If no data no seq number consumed

---
Connection Establisment
SYN flooding attack
- Malicious attackers send a large number of SYN segments faking IP addresses
- The server allocates resources which are never used until it runs out
- Denial of service attack
  - With so many requests the server may reject the valid ones
- Some implementations wait for the allocation until connection has been established

---
Data Transfer
Data sent in both
directions
ACKs piggybacked
with data

---
Data Transfer
- Pushing Data
  - Sender enables PUSH flag to request immediate response
  - Avoids waiting in the buffers
- Urgent Data
  - When some bytes are urgent
  - Receiver sets URGENT flag
  - Sender puts urgent bytes at the beginning of the segment
  - Sender sets urgent pointer at the end of the urgent data
  - The rest of the data are nonurgent

---
Connection Termination
Three way handshaking
Consumes 1 seq number if no data is carried

---
Connection Termination
Half Close

---
Normal Operation

---
Lost Segment

---
Reliable protocols

---
Reliable protocols
Let's analyze how to provide reliability
- From the simplest case to a real one, increasing the complexity
  - Simple protocol
  - Stop & wait
  - Go back N

---
Simple protocol
- Connectionless
- Assumes ideal conditions
- No error nor flow control are required
- Not realistic at all

---
Simple protocol
Flow diagram

---
Stop & Wait
- Connection-oriented
- Error and control flow
  - Acknowledgement for each packet
  - Checksum to check integrity
  - Sequence numbers
    - Requires a sliding window of size 1
  - timer
- Sender waits for reception of ACKs before sending a new packet

---
Sliding Window
- Sequence numbers use modulo 2m
  - Size of the window N = 2m-1
- While there's room inside the window new packets can be sent
- An ACK makes the window slide
Sliding direction

---
Stop & Wait
Flow diagram
ACK announces
the next packet
expected

---
Go Back N
- Waiting for a frame to be ack'd before sending a new one implies little channel efficiency
- To improve efficiency the channel must be pipelined
  - Continuous flow of requests
  - Some may be pending the acknowledge
  - Errors may force to go back and retransmit more than one frame
- Sliding window
  - More than one pending frame
  - N bits required for 2m-1 window size (sequence numbers)

---
Go Back N

---
Go Back N
m = 3
window size = 23 -1 = 7
for the sender
Window size = 1
for the receiver

---
Go Back N