application
Introduction to
Network Architecture
transport
network
link
physical
JuanPablo.Rozas@uclm.es David.Villa@uclm.es

---
Outline
- What is a network?
- Network classification
- Inter-networks
- Networking issues
- Packet switching modes
- Network architectures
- Reference models
  - OSI model
  - TCP/IP model
- Addressing fundamentals
- References

---
Internet today
ISP
Forouzan 5ed

---
Internet: administration
Forouzan 5ed
ISOC Internet Society
IETF Internet Engineering Task Force
IESG Internet Engineering Work Group
WG Work Group
RFC

---
Request for Comment (RFC)
Forouzan 5ed

---
What is a network?
- It is a set of interconnected autonomous computers so they may interchange information.
- The network users are aware that there are different computers with associated resources.
The network is usually represented by a cloud, to emphasize that we do not know its internal structure.
i

---
Network classification
- By link type
- By scale
- By topology

---
Networks
by link type
- A point-to-point connection provides a link that can only be used by the two peers.
- Usually they are wires, but microwaves or satellite links are also feasible.

---
Networks
by link type
- In a multipoint connection several nodes (more that two) share a link.
- Usually, it allows different addressing methods:
  - Unicast. The address identifies a single destination host.
  - Broadcast. A special address identifies all hosts in the net.
  - Multicast. The address identifies a host subset.

---
Networks
by scale
- IPN: InterPlanetary and Delay Tolerant Networks (DTN).
- Global (Internet).
- WAN: Wide Area Network – a country or intercontinental links.
- MAN: Metropolitan Area Network – A city or part of it.
- LAN: Local Area Network – A department or building.
- PAN: Personal Area Network – Computer and desktop.
- SAN: System Area Network – Clusters and embedded systems.
- NoC: Network On Chip – Network concepts inside a chip.

---
Networks
by scale: LAN
- The LAN is privately administered.
- High speed (100Mbps – 1Gbps), focused on resource sharing and the needs of a set of people.
- It uses a single transmission technology and topology.

---
Networks
by scale: WAN
- It involves hosts and sub-networks (that use p-t-p links).
- A subnet is composed by:
  - Link lines
  - Routers
router
router
The router must store messages and forward them to the appropriate destination. That “store and forward” mechanism (or “packet switching”) is the opposite of “circuit switching”.
Other example net
subnet

---
Networks
by topology
Star
Bus
Fully connected mesh
n(n-1)/2 links
Ring

---
inter-networks
- An inter-network is a set of interconnected (heterogeneous) networks.
- Networks with different software and hardware technology may share information due to a logical network protocol and gateways.

---
Networking main issues
- Addressing
- Errors detection and correction
- Message ordering
- Flow control
- Fragmentation
- Multiplexing
- Routing
- ...

---
Physical switching networks
Circuit Switching Network
The “old” telephone system
End to end
3 phases: Call (connection), talk, hook (disconnection)
Message Switching Network
The “old” telegraph system
End to post, post to post,... post to end
1 phase: message interchange
Packet Switching Network
Similar to the postal service
“Modern” computer networks

---
Comparing
circuit switching
message switching
packet switching
Tanenbaum

---
Packet switching modes
Today “all” computer networks
Similar to the postal service
Message is chopped in small messages called:	PACKET
Forouzan 5ed

---
Packet switching modes
Forouzan 5ed

---
Packet switching modes
Connectionless
Each packet is sent as a unrelated individual unit. The message includes destination (and probably source) address and other information for its delivery.
Connection-oriented
It requires a connection set-up phase, then the communication works as a continuous byte stream, usually supporting duplex transmission. End disconnection.

---
Network architecture
- It is a framework that describe a communication network, its components and protocols.
- The network design is organized as a layer stack.
- Each layer provides a set of services to the upper layer and requires services to the lower layer.
- The layer 'n' of a node maintains a virtual conversation with the same layer the destination node. That conversation must meet a specific protocol.

---
 Example of layering
Philosophers Analogy
Tanenbaum

---
Reference models
- OSI model
- TCP/IP model
The reference model and the protocol suite implementation are very different things. They must not be confused.
i

---
OSI model
- The Open System Interconnection (OSI) is an ISO (International Organization for Standardization)
- It provides a general conceptual model to describe and study any protocol stack.
- The model defines three basic concepts:
  - service: the function that a layer may provide.
  - interface: the way to get the layer services.
  - protocol: the set of rules between homologous peers.

---
OSI layering
application
application
presentation
presentation
session
session
transport
transport
network
network
link
link
physical
physical
physical media
bits
frames
packets
segments

---
OSI model
media layers
1. Physical layer
It defines the electrical, mechanical and temporal characteristics for devices required in a particular data communication technology.
2. Data link layer
It supports data transfers between directly reachable nodes (neighbors). It provides physical addressing.
3. Network layer
It supports end-to-end communication with variable length individual messages. It provides the logical addressing.

---
OSI model
host layers
4. Transport layer
It provides a reliable error-free communication channel between end users. It also support process multiplexing.
5. Session layer
It allows us to create sessions among hosts and it manages synchronization.
6. Presentation layer
It defines on-the-wire data representation and its semantic.
7. Application layer
Application specific protocols like mail, news, remote shell, etc.

---
TCP/IP model
- The TCP/IP model arrives years later of first implementations. The aim is to formalize and standardize its use and development.
- It is closely related with TCP/IP protocols stack, and it can not be used to describe other protocols or networks.
application
transport
inter-net
host to net

---
TCP/IP model
Application layer
High level protocols like: DNS, SMTP, HTTP, FTP and many others.
Transport layer
It defines transport protocols: TCP (Transport Control Protocol) and UDP (User Datagram Protocol).
Inter-network layer
It provides mechanisms to network interconnection and package routing. It defines the IP protocol, that provides a connectionless delivery service.
Host-to-net layer
It provides (does not provide) required mechanisms to make it possible that “an IP packet reaches other host in the network”.

---
OSI, TCP/IP and hybrid models
OSI
TCP/IP
hybrid
application
application
application
7
presentation
6
session
5
transport
transport
transport
4
network
inter-net
network
3
host to net
data link
data link
2
physical
physical
1
When we talk about a “x layer thing”
we always refer to the OSI model.
Although... we will use the hybrid.
i
i

---
Encapsulation
The user information can not go directly “on the wire”.
Data transmission requires group bytes in PDUs (Protocol Data Units). The PDU adds control information as header and tails.
user data
transport
header
segment
network
header
packet
link
header
tail
frame
bits
physical
data link
network
transport
application
physical
data link
network
transport
application

---
Encapsulation
The recipe
1. Data build (from an application).
2. Segment the data for end-to-end transportation.
3. Add network addresses and build one (or several) datagrams.
4. Add physical link address and build frames for each datagram.
5. Code frame bits in signals that can be sent by the physical medium.

---
ASCII table
Redes de Computadores I

---
Example: UDP encapsulation
Send the string “Redes~I” using UDP as transport protocol from port 57000 to port 8888, from IP address 161.67.27.124 to 161.67.48.57. The host MAC address is 00:21:5D:E9:7F:80 y the router’s MAC address is 00:64:40:3A:C9:40. All values are in hexadecimal
<............................................……......... 64 Bytes …............................................................>
<.. 7 Bytes ..>
User data:
52..............49
Padding:
00...........00
<..... 8 Bytes ….>
User
Datagram
Transport header:
DE.................E9
52.............49 00............00
<.... 20 Bytes ....>
Network header:
4500.............7C
IP datagram
DE................E9 52.............4900..............00
<......................................... 46 Bytes ……............................>
<... 14 Bytes ...>
<.. 4 Bytes..>
Data-Link header:
0064.........0800
Tail:
XXXXXXXX
Ethernet
frame
4500...............7C DE.............E952................4900...............00
bits
Redes de Computadores I
physical
data-link
network
transport
aplicación
physical
data-link
network
transport
aplicación

---
Encapsulation overview
Redes de Computadores I

---
Example: UDP encapsulation
Redes de Computadores I

---
Example: IP encapsulation
Redes de Computadores I

---
Example: Ethernet encapsulation
Redes de Computadores I

---
Addressing fundamentals
- Physical vs logical addresses
  - Lower-level layers vs higher-level layers.
  - Global uniqueness vs network-wide uniqueness.
  - Can’t be changed vs change frequently.
Tannenbaum

---
Physical address
Physical address = MAC address = Ethernet address
Tannenbaum

---
Logical address or IP address
A: source IP
P: destination IP
Tannenbaum

---
References
B.Forouzan. Transmisión de datos y redes de comunicaciones, 3th edition 2007.
Chapter 1
A.S.Tanenbaum Redes de computadoras. Pearson, 4th edition, 2003.
Chapter 1: Sections 1.1 a 1.4 y 1.6
CISCO Systems. Inc. Guía del primer año. CCNA 1 y 2. Cisco Press, 2003.
- Chapter 1
- Chapter 2: Pages 39 – 69
CISCO Networking Academy e-learning.
Modules 1 y 2.
    All unlabeled figures are taken from the Wikipedia.

---
CISCO Icons
Bridge
hub
switch
multilayer
switch
router
PC
dumb terminal
laptop
file server
FDDI ring
serial line
circuit switched
serial line
network cloud
Ethernet
FDDI